## Slide 1: Design Plan Flux Capacitors
Ryan Kachline, Calvin Nelson

## Slide 2: 1. Problem Statement
On an older car lacking electronically triggered ignition, all of the ignition timing alterations are done mechanically. They mainly operate in response to intake plenum pressure changes, or engine speed changes. We would like to invent a device that would allow the ignition timing to be further modified in response to up to 6 analog electrical sensors.
This is useful, in cases when you install power adders, such as a supercharger(s), turbocharger(s), and/or nitrous oxide to a car. In these cases, the thermal expansion rate of the combustion charge is increased. At low RPM when the engine does not feel the effects of a power adder, you want the ignition timing to act like a stock car. Alternatively, at higher RPM and/or when the power adder becomes active, you want the ignition timing to take into account this increased rate of thermal expansion.
This can be accomplished a number of ways, one example being factoring in the incoming air temperature. As the incoming air temperature increases, so does the rate of thermal expansion. Also, as a safeguard to the engine, devices called knock sensors can be added to the equation as well. Knock is when the ignition timing happens early enough that the maximum force applied by the combustion charge happens before the piston reaches the top of its compression stroke. This can be extremely harmful to an engine, and prevention of it is paramount. Clearly this device is useful in the cases explored above.

## Slide 3: 2. Proposed Solution
This device is meant to be installed in series with the conventional mechanically triggered ignition system. The device will use the mechanical trigger, and information from analog sensors to alter the phase. Once installed the user will be able to configure up to 6 analog sensors to alter the timing as they choose.
The device will:
Apply an ignition delay with a minimum step value of 0.5 degrees for a maximum operating speed of 6000 revolutions per minute.
The device will have a maximum timing retard of 30 degrees.
Use an Arduino Uno, and involve the design and implementation of a printed circuit board.
Be able to function in an automobile using automobile power supply (car battery).

## Slide 4: 3a. Design Approach
The device will follow the following algorithm:
1. Check push button state
2. Perform calculation for requested delay.
3. Wait for ignition event.
4. Delay for requested number of degrees.
5. Send ignition event.
6. Repeat.

## Slide 5: 3b. Technical Details
Assuming that the engine will have a maximum operating speed of 6000 revolution per minute, and the engine will be a 4 stroke, 8 cylinder engine, our worst case time between ignition events will be:
This means that the microcontroller in the Arduino will have the following number of cycles to calculate the following ignition delay:
Assuming that the minimum step amount of angular ignition delay is 0.5 degrees, the minimum step length at 6000 revolution per minute, will be:
The Arduino is accurate for any delay above 3 microseconds. Therefore it will suit our needs.

## Slide 6: 3b. Technical Details (cont.)
In our first design, we will have a push button which will trigger a static ignition delay. As we add stretch goals, the number of signals being processed increases. This will be an issue, because we will quickly reach the extent of the Arduino Uno.
Another issue that could arise is the cleanliness of the ignition signal. To remedy this, we will attempt to design a filter. This inherently will add delay, and we will evaluate that when we come to it.

## Slide 7: 3c. Manpower
Calvin Nelson – Gathering data from vehicle, testing, writing/editing reports
Ryan Kachline – PCB Design, writing/editing reports

## Slide 8: 3d. Schedule
EE 403W Flux Capacitors, Ignition Timing Delay Box (ITDB) Spring 2016 Schedule |  |  | 
Week | Monday Lab 2:30PM- 4:25PM 301 EEW | Wednesday Lab 2:30PM- 4:25PM 301 EEW | Notes
2/1/2016 | Aquire Microcontroller, Probe Ignition on Car |  | 
2/8/2016 | Preliminary Design |  | 
2/15/2016 | Have Working Push button Delay |  | 
2/22/2016 | Design Power filter, Milestone Report |  | 
2/29/2016 | PCB Design |  | 
3/7/2016 | Spring Break | Spring Break | Spring Break

## Slide 9: Schedule (cont.)
3/14/2016 | Assembly
3/21/2016 | Packaging Design
3/28/2016 | Stretch Goals
4/4/2016 | Stretch Goals, Milestone Report
4/11/2016 | Stretch Goals
4/18/2016 | Stretch Goals
4/25/2016 | Stretch Goals, Final Review

## Slide 10: 3e. Cost Estimate

## Slide 11: References

## Slide 12: References (cont.)

## Slide 13: Final Remarks